## Slide 1: SSI & Open Sound Control
Johannes Wagner
05.02.2013

## Slide 2: Architecture
Application
Sensors
Processing
Communication
SSI
S
S
OSC
Receiver
UDP/TCP

## Slide 3: Open Sound Control (OSC)
Transport-independent and message-based light ware protocol to share data between multimedia devices
Similar to MIDI but more powerful
Free implementations available for all kind of systems and languages
Website: http://opensoundcontrol.org/

## Slide 4: OSC Messages
Starts with an OSC Address Pattern followed by an OSC Type Tag String and a corresponding number of OSC Arguments
Int32: 32-bit big-endian two's complement integer
Float32: 32-bit big-endian IEEE 754 floating point number
OSC-string: A sequence of non-null ASCII characters followed by a null
OSC-blob An int32 size count, followed by that many 8-bit bytes of arbitrary binary data

## Slide 5: Specification
Based on UDP and OSC
Three type of messages: /strm continuously data stream /evnt event-related data including tags /text text based control messages
Each message has sender id and timestamp in order to synchronize messages

## Slide 6: Stream
Pattern | Arguments | Type | 
/strm | id time sr num dim bytes type data | String Int32 Float32 Int32 Int32 Int32 Int32 Blob | Identification Time in milliseconds Sample rate in Hz Sample number Sample dimension Size of a single sample value in bytes Sample type Byte array with data (interleaved)
SSI_UNDEF = 0,
SSI_CHAR = 1,
SSI_UCHAR = 2,
SSI_SHORT = 3,
SSI_USHORT = 4,
SSI_INT = 5,
SSI_UINT = 6,
SSI_LONG = 7,
SSI_ULONG = 8,
SSI_FLOAT = 9,
SSI_DOUBLE = 10,
SSI_LDOUBLE = 11,
SSI_STRUCT = 12,
SSI_IMAGE = 13,
SSI_BOOL = 14
Sample types:

## Slide 7: Stream Example
Sending head position as pair of integer values sampled at 30 fps, e.g.
sample 0 1 2 3 4 X 20 20 14 11 10 Y 10 10 11 9 9
/strm “head” 0 30.0 5 4 5 <data> where <data> has a total size of 4x4x5 bytes, e.g.: {80, [20 10 20 10 14 11 11 9 10 9]}

## Slide 8: Event and Text
Pattern | Arguments | Type | 
/evnt | id time duration state num eventTag_1 eventValue_1 … eventTag_num eventValue_num | String Int32 Int32 Int32 Int32 String Float32 String Float32 | Identification Time in milliseconds Duration in milliseconds Event state (0=completed,1=continued) Number of following events Tag of first event Value of first event Tag of last event Value of last event
/text | Id Time Duration Message | String Int32 Int32 String | Identification Time in milliseconds Duration in milliseconds Message content

## Slide 9: Event and Text Example
Sending key words and probabilities detected in interval [3.0 5.5]s (event is completed)
/evnt “words” 3000 2500 0 3 “I” 0.7 “feel” 0.4 “good” 0.9
Sending key words as message: /text “words” 3000 2500 “I feel good”

## Slide 10: sockspy
Tool for monitoring messages and data
Plain messages:
sockspy --simple <port>
OSC messages: sockspy --osc <port>
- ascii : log stream - console : output data on console